## Slide 1
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE 2026
NETRA
Offline AI Vision Assistant for Snapdragon PCs
An accessible, 100% on-device perception engine converting live camera feeds into real-time spoken descriptions via YOLOv8 object detection, EasyOCR, and native Windows SAPI TTS.
Target Hardware: Qualcomm® Snapdragon® Copilot+ PCs | Submission Package

## Slide 2
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
The Problem: Visual Information Friction in Daily Life
01. Reading Printed Text
Over 2.2 billion people live with vision impairment. Identifying medication dosages, food labels, warning signs, and printed documents creates daily accessibility barriers.
02. Cloud & Network Latency
Existing visual assistant apps depend heavily on cloud LLM APIs, causing high latency, recurring subscription costs, and complete failure during network outages.
03. Privacy & UI Complexity
Streaming live camera feeds to third-party cloud servers poses severe privacy risks. Complex touch interfaces are unusable for individuals requiring instant audio feedback.

## Slide 3
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
The Solution: Netra Offline AI Perception Engine
100% Offline Vision Assistance
• Zero Cloud Dependency: All processing runs locally on the host PC.
• Zero Subscription Fees: Open-source local perception pipeline.
• Privacy-First Telemetry: Camera frames never leave local memory.
• Instant Audio Feedback: Designed for single-key hands-free operation.
Multi-Modal Local Fusion
• Object Recognition: YOLOv8-N ONNX detects physical items & bounding boxes.
• Printed Text OCR: EasyOCR extracts labels, signs, and document text.
• Local Composition: Rule-based synthesis avoids LLM hallucination.
• Native Speech Output: Windows SAPI speaks clear audio descriptions.

## Slide 4
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
How Netra Works: 5-Stage Local AI Pipeline
1. Camera Capture
Webcam Video Input (DirectShow / OpenCV)
2. Object Detection
YOLOv8-N ONNX (Bounding boxes & labels)
3. Text Recognition
EasyOCR Engine (Printed text extraction)
4. Local Synthesis
Response Composer (Natural sentence merger)
5. Spoken Output
pyttsx3 / SAPI (Native Windows TTS)

## Slide 5
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
Technical Architecture & Component Stack
Core Application: Python 3.10 / OpenCV 5.0
Handles camera feed, bounding box overlay, keybindings, and high-contrast dashboard UI.
Inference Engine: ONNX Runtime 1.23
Pre-configured for Qualcomm QNN Execution Provider (Hexagon NPU) with CPU fallback.
Vision Perception: YOLOv8-N ONNX (12.26 MB)
Compact 80-class object detector running letterbox preprocessing and NMS postprocessing.
OCR & Speech: EasyOCR + pyttsx3 / SAPI
Fully offline text extraction and native Windows speech synthesis without cloud latency.

## Slide 6
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
Accessibility Focus & Real-World Use Cases
Medication & Label Reading
Point camera at prescription bottles or packages; Netra identifies the bottle and reads dosage text out loud.
Object & Obstacle Identification
Recognizes physical objects (chairs, cups, laptops, keys) in immediate surroundings to aid navigation.
Signage & Directional Guidance
Extracts room numbers, office door signs, and printed directions for low-vision individuals.
Zero-Telemetry Privacy
Operates entirely offline, guaranteeing personal camera feeds remain strictly private on-device.

## Slide 7
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
Qualcomm® Snapdragon® Hardware Strategy & Verified Status
Qualcomm QNN EP Strategy
• Qualcomm QNN Integration: Engine requests QNNExecutionProvider (QnnHtp.dll burst mode) targeting Hexagon NPU.
• Snapdragon Copilot+ Target: Designed for ARM64 Snapdragon Windows PCs with onnxruntime-qnn installed.
• Graceful Fallback: Seamlessly defaults to CPUExecutionProvider on non-Snapdragon host development machines.
Empirical Verified Metrics
• Detection Latency: ~40.1 ms average inference time (~25 FPS) on host processor.
• Model Footprint: Compact YOLOv8-N ONNX binary requires only 12.26 MB storage.
• Zero API Dependency: Entire visual perception turn completes locally without internet access.

## Slide 8
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
Live Demonstration Sequence & User Interface
Step 1: Launch App
Double-click run.bat or execute python main.py. App initializes camera and local models.
Step 2: Interactive Overlay
High-contrast dark dashboard opens displaying real-time camera view and status panel.
Step 3: Press SPACE Bar
Captures frame, runs object detection + EasyOCR, composes description, and speaks out loud.

## Slide 9
QUALCOMM® SNAPDRAGON® AI LAB CHALLENGE
Core Innovation & Project Differentiation
Zero-Cloud Local Pipeline
Complete perception and speech synthesis execute locally on-device with zero cloud telemetry.
Ultra-Low Storage Footprint
Sub-15 MB total model binaries ensure low memory overhead and rapid cold-start times.
Deterministic Response Merger
Synthesizes visual bounding boxes and OCR text into natural sentences with zero LLM hallucination.

## Slide 10
QUALCOMM® SNAPDRAGON® AI LAB BUILD & PRESENT CHALLENGE
NETRA: "See it. Understand it. Hear it."
Empowering independence for low-vision users through Snapdragon-powered on-device AI.
Thank You! Submission package prepared for review.